## Slide 1: CA LAB(13) ESP8266 Wifi Module

## Slide 2: Problem
We want to connect our MCU (Arduino) with Internet
Why we want Internet connection with Arduino?
To control and gather data from remote locations.
For communication purpose
To utilize existing infrastructure & protocols
For IoT

## Slide 3: Connection with Internet
Arduino can connect with Internet through these ways
Ethernet
WiFi
3G,4G,GSM

## Slide 4: Ethernet

## Slide 5: WiFi

## Slide 6: 3G,4G

## Slide 7: ESP8266

## Slide 8: ESP8266
A popular and cheap module of WiFi for arduino
Simple serial interface
Operates on 3.3V more then 3.3V will damage the board. (Very sensitive)
AT commands
Has it’s own firmware and also can be programmed
Different operating modes

## Slide 9: ESP8266 Pinout

## Slide 10: ESP8266 Pinout
VCC for power connected with 3.3V
GPIO0 and GPIO2 are general purpose digital ports. GPIO0 also controls the module mode (programming or normal operation).
Rx is the receiver pin
Tx is the transmitter pin

## Slide 11: ESP8266 Pinout
CH_PD: Chip enable. Keep it on high (3.3V) for normal operation.
RST: Reset. Keep it on high (3.3V) for normal operation. Put it on 0V to reset the chip.
GND is ground.

## Slide 12: Node MCU

## Slide 13: Node MCU
• Voltage:3.3V.
• Wi-Fi Direct (P2P), soft-AP.
• Current consumption: 10uA~170mA.
• Flash memory attachable: 16MB max (512K normal).
• Integrated TCP/IP protocol stack.
• Processor: Tensilica L106 32-bit.
• Processor speed: 80~160MHz.
• RAM: 32K + 80K.
• GPIOs: 17 (multiplexed with other functions).
• Analog to Digital: 1 input with 1024 step resolution.
• +19.5dBm output power in 802.11b mode
• 802.11 support: b/g/n.
• Maximum concurrent TCP connections: 5.

## Slide 14: ESP8266 WiFi Modes
1. Access Point (AP) :In AP the Wi-Fi module acts as a Wi-Fi network, or access point (hence the name), allowing other devices to connect to it. It establishes a two-way communication between the ESP8266 and the device that is connected to it via Wi-Fi.

## Slide 16: ESP8266 WiFi Modes
2. Station (STA) :In STA mode, the ESP-01 can connect to an AP (access point) such as the Wi-Fi network from your house. This allows any device connected to that network to communicate with the module.

## Slide 18: ESP8266 WiFi Modes
3. Both: In this mode ESP-01 act as both an AP as well as in STA mode.

## Slide 19: Install the ESP8266 Board Package
In Arduino IDE goto file option and click on the preferences.
A new window will pop up in the settings Enter http://arduino.esp8266.com/stable/package_esp8266com_index.json into Additional Board Manager URLs.

## Slide 22: Click ‘Tools’ -> ‘Board:’ -> ‘Board Manager…’ to access this panel. In search type ESP8266

## Slide 25: ESP8266
Now we will look how to establish connection of ESP8266 with Thingspeak using arduino